## Slide 1
NXP DIGITAL TWINS
Turn Zephyr board metadata into vivid, actionable digital twins
Discover boards. Seed twins. Derive custom hardware. Close the loop with real lab validation.
81
NXP boards indexed
81
twin seeds
1
custom boards
Why this matters
Move from board folders to machine-readable engineering knowledge
Create board-level twins before hardware is fully stable
Bridge software, validation, and lab operations in one flow
nxp_digital_twins • overview
1

## Slide 2
The engineering gap we wanted to close
Before
Board knowledge lives in DTS, YAML, Kconfig, support scripts, and docs
Target variants are easy to miss across cm4/cm7/ns/qspi/smp/ddr flavors
Custom board spin-offs repeat manual copy/rename work
With nxp_digital_twins
Board inventory becomes structured JSON and readable reports
Every board gets a twin seed with capabilities, targets, and dev metadata
Custom boards can inherit from proven Zephyr reference designs
Impact
Faster board selection
Traceable customization
Better lab readiness
Cleaner automation handoff
nxp_digital_twins • problem statement
2

## Slide 3
What is inside the nxp_digital_twins project
tools/
generate_nxp_board_knowledge.py
create_custom_board.py
create_zephyr_custom_board.py
Scripts turn source trees into reusable artifacts
skills/
board_selection.md
twin_modeling_workflow.md
custom_board_derivation.md
Human-readable playbooks for repeatable engineering flows
knowledge/
nxp_board_inventory.json / .md
nxp_digital_twin_seeds.json
twins/dg_evk.json
custom_boards_index.json
nxp_digital_twins • structure
3

## Slide 4
From Zephyr board folders to an NXP board landscape
81
boards discovered
81
seed objects generated
11
families classified
78
boards with docs
19
boards with board.c logic
Top families
board family distribution
MCX 19
IMX 16
MIMXRT 16
OTHER 10
LPCXPRESSO 8
Most common capabilities
capability frequency
gpio 69
i2c 64
spi 55
flash 55
counter 54
watchdog 53
nxp_digital_twins • inventory
4

## Slide 5
The digital twin pipeline
boards/nxp Zephyr source
knowledge generator
inventory + seed models
custom board derivation
lab validation and iteration
One stream converts board metadata into digital twin knowledge; the second stream turns those twins into custom board programs and validation loops.
nxp_digital_twins • pipeline
5

## Slide 6
Anatomy of a board twin seed
Example base twin: mimxrt1170_evk
Twin id: nxp.mimxrt1170_evk
Family: mimxrt
Architectures: arm
Targets: 4
Capabilities include: adc, can, counter, dac, display, dma...
Development section carries toolchain and board source path
Lab profile can attach real flash and remote execution details
seed shape
{
"twin_id": "nxp.mimxrt1170_evk",
"classification": {"family": "mimxrt"},
"hardware": {
"socs": ["mimxrt1176"],
"targets": [".../cm4", ".../cm7"]
},
"capabilities": ["adc", "can", "netif:eth", "video", ...],
"development": {"toolchains": ["zephyr", "gnuarmemb"]},
"lab_profile": {...}
}
nxp_digital_twins • seed anatomy
6

## Slide 7
Custom board derivation: from mimxrt1170_evk to dg_evk
Base board
Zephyr reference: mimxrt1170_evk
Twin seed already contains targets, capabilities, and lab profile
Used as the inheritance anchor
Derived twin
New board name: dg_evk
Twin id: nxp.dg_evk
Target identifiers rewritten to dg_evk/*
Derivation metadata preserved for traceability
Generated board scaffold
boards/nxp/dg_evk created from mimxrt1170_evk
Kconfig, board.yml, DTS, YAML, docs renamed
Ready for real hardware delta edits
nxp_digital_twins • custom board
7

## Slide 8
How teams use it day to day
1) refresh the knowledge base
python digital_twins_nxp\tools\generate_nxp_board_knowledge.py --source C:\github\zephyrproject\zephyr\boards\nxp --outdir C:\github\zephyr_mcp\digital_twins_nxp\knowledge
2) derive a custom board twin
python digital_twins_nxp\tools\create_custom_board.py --seeds digital_twins_nxp\knowledge\nxp_digital_twin_seeds.json --base-board mimxrt1170_evk --new-board dg_evk --spec digital_twins_nxp\knowledge\dg_evk_spec.json --out digital_twins_nxp\knowledge\twins\dg_evk.json --index digital_twins_nxp\knowledge\custom_boards_index.json
3) generate the Zephyr board scaffold
python digital_twins_nxp\tools\create_zephyr_custom_board.py --source-dir C:\github\zephyrproject\zephyr\boards\nxp\mimxrt1170_evk --dest-dir C:\github\zephyrproject\zephyr\boards\nxp\dg_evk --base-board mimxrt1170_evk --new-board dg_evk --new-display-name DG-EVK --force
nxp_digital_twins • usage commands
8

## Slide 9
Closed-loop validation with the real lab
Embedded in the twin
SSH host: ubuntu@10.17.12.234
Remote Zephyr path: /home/shared/disk/zephyr_project/zephyr_test/zephyr
Serial path: /dev/serial/by-id/usb-NXP_Semiconductors_MCU-LINK_on-board__r0E2__CMSIS-DAP_V2.250_CMYBV2XFSPLRA-if02
Flash command: west flash --runner linkserver --probe "CMYBV2XFSPLRA"
example validation loop
ssh ubuntu@10.17.12.234
cd /home/shared/disk/zephyr_project/zephyr_test/zephyr
west build -b mimxrt1170_evk/mimxrt1176/cm7 samples/hello_world
west flash --runner linkserver --probe "CMYBV2XFSPLRA"
# observe serial and compare with twin expectations
nxp_digital_twins • lab integration
9

## Slide 10
High-value usage scenarios
Board selection
Find boards by capability
Compare families and targets
Start the right twin fast
Bring-up planning
See variants and support files
Identify initialization hotspots
Plan validation loops
Custom hardware
Clone from a strong base
Track derivation decisions
Keep twin and board in sync
Lab operations
Reuse flash commands
Attach remote host context
Close the loop with hardware
nxp_digital_twins • use cases
10

## Slide 11
What comes next
Engineering roadmap
Add higher-fidelity attributes: clocks, buses, power, connectors, sensors
Create per-board curated twins under knowledge/twins/
Add search and filtering by capability and family
Expand validation automation around build, flash, and runtime checks
Takeaway
nxp_digital_twins is a practical bridge from Zephyr board support to digital twin operations
It already supports discovery, seed generation, custom board derivation, and lab-aware validation
The next step is deeper board-specific enrichment, not reinventing the foundation
nxp_digital_twins • next steps
11